## Slide 1
DUNA
A desert race machine, re-engineered as software · A Baja / Dakar-class rally-raid race motorcycle · series-hybrid powertrain · full by-wire control · Confidential 2026

## Slide 2
01
The most advanced desert race machine on earth — and a new powertrain proven doing it

## Slide 3
THE THESIS
Rally-raid has never had a software-defined powertrain
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
A small engine runs at one fixed, most-efficient point as a generator only — no mechanical link to the wheel. It feeds a buffer battery and an electric motor that drives the rear wheel. The rider commands wheel torque; software commands everything else.
Instant, exact torque — slip control that clamps in a millisecond, not by fighting an engine
Range is a fuel-tank question, not a charging problem — refuels in the time it takes to pour fuel
Silent low-speed running on the buffer — a tactical stealth capability
Every component exists and is proven elsewhere. The innovation is integration, not invention.

## Slide 4
THE PERFORMANCE BAR WE RESPECT
Measured against the best 450 rally bikes on earth
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
139 kg
KTM 450 RALLY DRY WEIGHT — THE BAR (VERIFIED, KTM.COM)
~47 kW
KTM PEAK POWER — OUR ELECTRIC DRIVE EXCEEDS IT (86 KW PEAK MOTOR)
35 L
REFERENCE FUEL CAPACITY — RANGE = TANK SIZE
KTM 450 Rally Replica and Honda CRF450 Rally are the raceability reference — ~140 kg class, ~35 L fuel, hours at load in the heat, serviceable in a bivouac. Our answer is heavier by a known, quantified margin and defensible on handling, efficiency, and control.

## Slide 5
02
A category never re-invented, and a proving ground you can enter with one prototype

## Slide 6
WHY NOW
The software-defined powertrain moment has arrived
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
The parts are finally real
Axial-flux traction motors at 10 kg, 86 kW peak (EMRAX 208, VERIFIED)
Motorsport inverters at 6.75 kg, IP6K9K wash-rated (Cascadia CM200, VERIFIED)
High-rate 21700 cells at 231 Wh/kg (Molicel P45B, VERIFIED)
Compact rotary range-extenders that love one fixed RPM (Aixro XR50, VERIFIED)
The door is open
US desert racing (Baja 1000 / SCORE) — fewer rules constraints, a prototype can enter sooner: the near-term proving ground
Dakar Future / Mission 1000 — ASO's official hybrid & alternative-propulsion on-ramp (VERIFIED)
FIM already runs Equivalence-of-Technologies rules for electric vs ICE
Dakar is the aspirational ceiling. SCORE/Baja is where we prove it first.

## Slide 7
“Series hybrid turns every hard mechanical problem — traction, torque delivery, engine efficiency, thermal — into a software problem. It is a software-defined powertrain in a category that has never had one.”
THE INVESTABLE THESIS, IN ONE LINE
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM

## Slide 8
03
Ducati-grade design language over genuine desert race engineering

## Slide 9
Exposed Core, stealth graphite
The canonical form — battery low and central, no gearbox bulge, no top-end engine · Baja terrain

## Slide 10
THE ENERGY PATH
No gearbox, no mechanical link to the wheel
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
What the engine does
The APU runs at one fixed, efficient point and delivers a smooth ~12–15 kW. It never chases transients — it just holds its best-efficiency point. This is why a series hybrid is efficient in a spiky, stop-start duty cycle like rally.
What the battery does
A ~2.0 kWh buffer absorbs generator surplus and supplies bursts up to ~31 kW for dune climbs and launches. It is a shock absorber between a steady genset and a spiky wheel demand — a buffer, not an EV pack.

## Slide 11
THE CORE
The whole trick lives on one DC bus
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
Buffer pack in the frame, axial-flux motor, twin radiators. A single fixed reduction replaces the KTM's six-speed gearbox — an electric motor's flat torque curve removes the need for gears.
EMRAX 208 traction motor — 86 kW peak / 56 kW continuous, 10 kg
Cascadia CM200 inverter — 225 kW rated, 6.75 kg, wash-proof
96s2p Molicel P45B buffer — ~2.0 kWh usable, low and central
Aixro XR50 rotary as the generator — buyable today

## Slide 12
04
Once torque is a software variable, control is nearly free — and it compounds

## Slide 13
THE DEFENSIBLE STACK
Mechanical problems become software problems
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
Traction-by-wire
The VCU knows commanded torque, both wheel speeds, and lean angle in real time. Slip control clamps motor torque the instant the rear outruns a target slip ratio — roughly 100× faster than fighting an engine with ignition or a butterfly. Lean-sensitive torque and per-surface launch maps are trivial once torque is a software variable.
The compounding advantage
The engine's thermal load is decoupled from vehicle speed — the VCU can crawl on battery to shed heat, then restart
Torque maps per surface: sand, gravel, hardpack, rider-selectable
Two-motor torque vectoring (true AWD in sand) is a clean roadmap option
Every kilometre ridden makes the maps better — the software is the asset

## Slide 14
BY-WIRE CONTROL — PROTOTYPE-HONEST
What is mature, and what is the real work
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
Throttle-by-wire: dual-redundant grip sensors. Shipped on every premium bike today. Low risk.
Brake: prototype runs a conventional hydraulic front (fail-safe) blended with by-wire regen on the rear — the responsible choice for a solo high-speed machine. Full dry brake-by-wire is the named production path, not the prototype spec.
VCU: the brain — torque map, slip control, generator set-point, thermal management, regen blending. This is the single biggest build-cost line, and we treat it as such.
Safety-conscious architecture designed toward functional safety — HV interlock, pyro-fuse crash disconnect, redundant channels, watchdog. We do not claim certification on a prototype.

## Slide 15
05
The honest numbers — because the answers survive a mechanical engineer in the room

## Slide 16
THE HONEST WEIGHT VERDICT
~+18 kg dry (~+13% vs KTM) — quantified, not hidden
Sum of verified component masses + estimated structure. The penalty is powertrain duplication (both an APU and a full e-drive); the offset is that the heaviest item sits low and central, lowering CG.
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM

## Slide 17
THE STRUCTURAL ADVANTAGE
Range scales with the tank, not the battery
Want 500 km instead of 400? Add ~12 L (~9 kg) of fuel — not ~40 kWh of battery (~180 kg). This is the series-hybrid advantage, and it is real. Figures are engineering estimates from the master numbers (20 kW stage average, ~27% fuel-to-wheel).
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM

## Slide 18
NO PHYSICS WALL
Every component is real, spec'd, and proven elsewhere
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
157 kg
DRY MASS — RE-ADDED FROM VERIFIED COMPONENTS (EST)
~27%
FUEL-TO-WHEEL EFFICIENCY — THE MATH SHOWN, NOT OVER-CLAIMED (EST)
~40 L
DESIGN TANK FOR A ~340 KM SPECIAL — SCALES LINEARLY
The risk is integration, not invention. The three risks that actually decide this program are weight, controls software, and the stage-power assumption — each named, quantified, and with a concrete retirement plan on the timeline.

## Slide 19
06
The honest risk section is the credibility — nothing here is hand-waved

## Slide 20
THE THREE RISKS THAT DECIDE THE PROGRAM
Named, quantified, each with a retirement plan
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
We own the 20 kW assumption first, as a Phase-0 validation plan — not as an ambush. All range/fuel/APU math scales off it, and it is the one number diligence will push on.
Risk | Severity × likelihood | How it retires
Weight (+~13% vs KTM) | High × certain | Package all major mass low & central; model in multibody sim, then prove on a rider. Beat the KTM on handling, not the scale.
Controls software maturity | High × high | Develop maps on a dyno + HIL rig before open-desert running. The biggest cost line, treated as such.
The 20 kW stage-average assumption | High × medium | Phase-0 telemetry: data-log a real 450 at Baja pace before freezing APU & tank. Closeable in ~2 weeks.

## Slide 21
07
Prove the hardest subsystem in the cheapest, safest place first

## Slide 22
~18–24 MONTHS TO A RUNNING, SHAKEN-DOWN PROTOTYPE
Risk retires in the right order
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
Phase 0–1 — freeze & bench
Phase 0 (Mo 0–3): close the power assumption with telemetry, freeze BOM & voltage architecture, order long-lead items
Phase 1 (Mo 3–9): the powertrain runs on a bench — APU genset, buffer pack, motor + inverter on a dyno, VCU on HIL
Retires the fuel math and the bulk of the controls risk before anything moves
Phase 2–3 — roll & shake down
Phase 2 (Mo 6–15): CAD, CG/handling sim, fabricate chassis, first rolling self-powered running
Phase 3 (Mo 15–24): dust + shaker durability, progressive desert testing, HV crash-safety, map refinement
Deliverable: a prototype that completes a representative stage — the data package for Mission 1000 and the next raise
Critical path: the APU generator integration and the controls software

## Slide 23
08
This raise buys a running proof-of-concept. The race program is the next raise.

## Slide 24
USE OF FUNDS — ONE RUNNING PROTOTYPE
~$0.75M buys one running proof-of-concept bike
Budgetary estimate for ONE proof-of-concept bike. Does NOT include a race season, a spare bike, a team, or homologation testing — those are the next raise. A prototype is dominated by engineering labor, not parts.
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM

## Slide 25
PHASED CAPITAL, STATED HONESTLY
A seed-stage number that proves the thesis
CONFIDENTIAL · 2026 · SERIES-HYBRID RALLY-RAID PROGRAM
~$0.75M
THIS RAISE — ONE RUNNING PROOF-OF-CONCEPT PROTOTYPE
18–24 mo
TO A SHAKEN-DOWN BIKE THAT COMPLETES A REPRESENTATIVE STAGE
Phase 2
THE RACE PROGRAM — THE NEXT, LARGER, DE-RISKED RAISE
A factory Dakar bike program runs into the tens of millions per season. A single innovative prototype at ~$0.75M is credible and modest against that — exactly what a venture investor funds to de-risk the next, larger raise.

## Slide 26
DUNA
The proving ground is open. The parts are real. The moat is the software.
A Baja / Dakar-class rally-raid race machine with the first software-defined powertrain in its category.
This raise builds the running proof-of-concept. The race program follows, de-risked.
Every load-bearing number traces to the feasibility dossier and its verified sources.
Confidential · 2026 · Numbers travel together with the feasibility dossier